## Slide 1: Long-Mann 16-Bit RISC Processor
Final DESIGN REVIEW presentation
Taylor Long, Jared Mann
Notes: Jared

## Slide 2: High Level Overview
Hierarchy and RTL SCHEMATIC
Notes: Jared

## Slide 3
FIRST STEPS – SIMPLE CPU, ALU, STARTING CONTROL UNIT AND PIPELINE STAGES
Notes: Jared – A month ago completed Labs, 3 weeks ago had simple cpu, Started Collaboration Through Github for having a backed up version of project, allowed us to work concurrently on different aspects of project, Keep ongoing documentation.

## Slide 4: THE FINISHED ALU
The ALU is capable of producing results in all modes
Multiplication is done by taking the 8 LSB’s of in1 and in2 and producing a 16-bit result
The ALU operates asynchronously, improving performance
Notes: Jared

## Slide 5: THE FINISHED ALU – RTL SCHEMATIC, PERFORMANCE
HDL Synthesis Report
Macro Statistics
# Multipliers : 1
8x8-bit multiplier : 1
# Adders/Subtractors : 1
16-bit addsub : 1
# Comparators : 1
16-bit comparator less : 1
# Logic shifters : 2
16-bit shifter logical left : 1
16-bit shifter logical right : 1
Timing Summary:
Speed Grade: -5
Minimum period: No path found
Minimum input arrival time before clock: No path found
Maximum output required time after clock: No path found
Maximum combinational path delay: 14.386ns
Notes: Jared – Each module we made was evaluated in RTL schematics to see if there were any glaring issues. This module had no latches.

## Slide 6: THE ROM FILE
The Contents of The ROM File are byte addressable, word aligned
Notes: Taylor

## Slide 7: THE ROM FILE – PERFORMANCE AND RTL SCHEMATIC
Timing Summary:
Speed Grade: -5
Minimum period: No path found
Minimum input arrival time before clock: 1.814ns
Maximum output required time after clock: 5.962ns
Maximum combinational path delay: No path found
Advanced HDL Synthesis Report
Macro Statistics
# RAMs : 2
255x8-bit single-port block RAM : 1
256x8-bit single-port block RAM : 1
Notes: Taylor.

## Slide 8
Development Timeline
FINISHING PIPELINE STAGES, RAM MODULE, BEGINNING HAZARDS
Notes: Taylor

## Slide 9: Pipeline Stages
ID/EXE
EXE/MEM
MEM/WB
IF/ID

## Slide 10: Pipeline Stages – Instruction Fetch / Instruction Decode

## Slide 11: Pipeline Stages – Instruction Fetch / Instruction Decode – RTL SCHEMATIC
Timing Summary:
---------------
Speed Grade: -5
Minimum period: 2.278ns (Maximum Frequency: 438.982MHz)
Minimum input arrival time before clock: 3.631ns
Maximum output required time after clock: 4.040ns
Maximum combinational path delay: No path found
=========================================================================
HDL Synthesis Report
Macro Statistics
# Registers : 34
1-bit register : 32
16-bit register : 2

## Slide 12: Pipeline Stages – Instruction DECODE / EXECUTION

## Slide 13: Pipeline Stages – Instruction DECODE / EXECUTION – RTL SCHEMATIC, PERFORMANCE
HDL Synthesis Report
Macro Statistics
# Registers : 69
1-bit register : 63
16-bit register : 3
3-bit register : 2
7-bit register : 1
Timing Summary:
---------------
Speed Grade: -5
Minimum period: 2.278ns (Maximum Frequency: 438.982MHz)
Minimum input arrival time before clock: 2.982ns
Maximum output required time after clock: 4.040ns
Maximum combinational path delay: No path found

## Slide 14: Pipeline Stages – EXECUTION / MEMORY

## Slide 15: Pipeline Stages – EXECUTION / MEMORY – RTL SCHEMATIC, PERFORMANCE
HDL Synthesis Report
Macro Statistics
# Registers : 52
1-bit register : 48
16-bit register : 2
3-bit register : 1
7-bit register : 1
Timing Summary:
---------------
Speed Grade: -5
Minimum period: 2.278ns (Maximum Frequency: 438.982MHz)
Minimum input arrival time before clock: 2.977ns
Maximum output required time after clock: 4.040ns
Maximum combinational path delay: No path found

## Slide 16: Pipeline Stages – Memory / Writeback

## Slide 17: Pipeline Stages – Memory / Writeback – RTL SCHEMATIC, PERFORMANCE
HDL Synthesis Report
Macro Statistics
# Registers : 31
1-bit register : 28
16-bit register : 1
3-bit register : 1
7-bit register : 1
Timing Summary:
---------------
Speed Grade: -5
Minimum period: 2.278ns (Maximum Frequency: 438.982MHz)
Minimum input arrival time before clock: 2.973ns
Maximum output required time after clock: 4.040ns
Maximum combinational path delay: No path found

## Slide 18: RAM MODULE
Due to hardware constraints our implemented RAM Module is not capable of accessing addresses
Writing to RAM is a synchronous process
Reading from RAM is an asynchronous process to improve read times

## Slide 19: RAM MODULE – PERFORMANCE
Timing Summary:
---------------
Speed Grade: -5
Minimum period: 10.625ns (Maximum Frequency: 94.120MHz)
Minimum input arrival time before clock: 8.257ns
Maximum output required time after clock: 4.040ns
Maximum combinational path delay: No path found
HDL Synthesis Report Macro Statistics # Adders/Subtractors : 1 8-bit adder : 1 # Registers : 272 1-bit register : 16 8-bit register : 256 # Multiplexers : 2 8-bit 256-to-1 multiplexer : 2
Notes: Only Performance Metrics Due To RTL Containing Every cell of Memory, we see that memory is the major limiting factor for speed, given more time optimization of memory would be the first place we would look for performance improvements.

## Slide 20
Development Timeline
FINISHING HAZARD DETECTION, STARTING BRANCH INSTRUCTIONS, STARTING USER I/O
Notes: Transition to Taylor

## Slide 21: DATA HAZARD DETECTION
6-Bit hazard signal is used to detect possible hazards for indicating the operand in question and the position in the pipeline for possible forwarding.

## Slide 22: Hex to Seven Segment Display Driver
The Display Driver was designed to only change what is displayed when the opcode indicates an OUT instruction.
Notes: Transition to Jared

## Slide 23: Hex to Seven Segment Display Driver – RTL and PERFORMANCE
Advanced HDL Synthesis Report
Macro Statistics
# FSMs : 1
# Latches : 1
16-bit latch : 1
Timing Summary:
---------------
Speed Grade: -5
Minimum period: 2.396ns (Maximum Frequency: 417.362MHz)
Minimum input arrival time before clock: 1.731ns
Maximum output required time after clock: 9.907ns
Maximum combinational path delay: No path found
Notes: Hex to Seven Seg Requires a latch for the user i/o switch, given more time would try to optimize all latches down

## Slide 24
Development Timeline
FINISHING L INSTRUCTIONS, USER I/O DEBUGGING, DATA FORWARDING
Notes: Taylor

## Slide 25: DATA FORWARDING
The hazard detection indicates where in the pipeline the hazard is. This determines where to forward data from to limit stalling as much as possible.

## Slide 26
Development Timeline
FINAL TOUCHES – BRANCH PREDICTIONS (COMPLETE), PROJECT REPORT WRITING, HARDWARE DEBUGGING (LATCH REDUCTION, RUNNING TEST CODE – ONGOING)

## Slide 27
FULL PROCESSOR SYNTHESIS SUMMARY (SUBJECT TO CHANGE)
Timing Summary:
Speed Grade: -5
Minimum period: 21.547ns (Maximum Frequency: 46.410MHz)
Minimum input arrival time before clock: 5.285ns
Maximum output required time after clock: 11.939ns
Maximum combinational path delay: No path found
Advanced HDL Synthesis Report Macro Statistics # FSMs : 1 # RAMs : 2 255x8-bit single-port block RAM : 1 256x8-bit single-port block RAM : 1 # ROMs : 1 16x3-bit ROM : 1 # Multipliers : 1 8x8-bit multiplier : 1 16-bit 4-to-1 multiplexer : 1 3-bit 4-to-1 multiplexer : 3 # Logic shifters : 2 16-bit shifter logical left : 1 16-bit shifter logical right : 1 | # Adders/Subtractors : 3 16-bit adder : 1 16-bit addsub : 1 8-bit adder : 1 # Registers : 2540 Flip-Flops : 2540 # Latches : 5 1-bit latch : 2 16-bit latch : 2 3-bit latch : 1 # Comparators : 12 16-bit comparator equal : 1 16-bit comparator less : 1 16-bit comparator not equal : 1 3-bit comparator equal : 9 # Multiplexers : 70 1-bit 256-to-1 multiplexer : 16 1-bit 4-to-1 multiplexer : 18 1-bit 8-to-1 multiplexer : 32

## Slide 28: Looking Back – All Goals Met
Implemented a RISC like 16-Bit Processor
The Processor is capable of handling all instruction types
The Processor implements a 5-Stage Pipeline Design
FINAL SUMMARY – PROBLEM SOLUTION

## Slide 29: Group Project Choices / Additional Features
Implemented Branch Prediction (Branch Not Taken Assumption)
Implemented Data Forwarding
Implemented User I/O, holding the process to allow for user input, pressing a button to continue until next user input, or output display
FINAL SUMMARY